## Slide 1: Scaling the Memory Power Wall with DRAM-Aware Data Management
Raja Appuswamy
Matthaios Olma
Anastasia Ailamaki
Ecole Polytechnique Fédérale de Lausanne (EPFL)

## Slide 2: Power-Hungry MMDBs?
Year | End-use Energy B kwh | Elec. Bills ($B) | Power plants (500MW) | CO2 (US) Million MT
2013 | 91 | $9.0 | 37 | 97
2020 | 139 | $13.7 | 51 | 147
2013-2020 incr. | 47 | $4.7 | 17 | 50
Energy efficiency - The New Holy Grail
What is the energy behavior of MMDBs?

## Slide 3: Energy in MMDB
Chart: DRAM total capacity
| 8GB | 16GB | 32GB | 64GB | 128GB | 192GB | 256GB | 384GB | 512GB | 768GB | 1TB | 1.5TB | 2TB | 3TB | 4TB | 6TB
DRAM Idle (Watt) | 1.21 | 1.01 | 2.02 | 4.04 | 7.27 | 12.11 | 14.53 | 21.79 | 29.04 | 43.56 | 58.11 | 87.33 | 116.81 | 176.62 | 319.86 | 442.95
DRAM Loaded (Watt) | 5.53 | 5.12 | 5.53 | 10.24 | 15.58 | 30.84 | 31.25 | 47 | 62.82 | 94.7 | 126.83 | 191.62 | 256.71 | 386.43 | 618.15 | 895.85
4P Loaded (W) | 352.03 | 352.03 | 352.03 | 352.03 | 352.03 | 352.03 | 352.03 | 352.03 | 352.03 | 352.03 | 352.03 | 352.03 | 352.03 | 352.03 | 352.03 | 352.03
*HP Power advisor, six-core Intel Xeon E7-4809v2
4-socket - 24 cores, 96 DIMM slots
2.5x loaded
CPU Loaded (Watt)
1.25x idle
16x capacity
3x power
4x capacity
10x power
DRAM will emerge as a major contributor

## Slide 4: Server Memory Trends
Memory Type | Max Capacity | Latency (nsec) | Bandwidth (GB/s) | Loaded W/GB | Idle W/GB
UDIMM | 128 | 153.7 | 72 | 0.2 | 0.02
LRDIMM | 768 | 235 | 40.4 | 0.15 | 0.07
HCDIMM | 768 | 161.9 | 63.9 | 0.74 | 0.37
Processor: Intel Xeon E5 2 sockets, 4 channels/socket
Capacity – Performance Tradeoff
Capacity – Power Tradeoff
Capacity Limitation
Big data => Big memory => Big power bills
MMDBs should focus on reducing DRAM power

## Slide 5: Reducing DRAM Power Draw
Hardware features
  Frequency scaling
  Power-down modes
Limitations
  Enabled/disabled statically at boot time
  Power-down state transition controlled by MC
What is the impact on MMDB performance?
What is the effectiveness under MMDB workloads?

## Slide 6: Experimental Setup
Hardware
  2 GHz Intel Xeon E5-2640 v2 CPU (2 socket, 8 cores/socket)
  256 GB of memory (16x 16 GB RDIMMs)
Micro-benchmarks
  Concurrent Scans 128 MB of int64s
  Parallel Aggregation (a = ∑(b(i)+c(i))) over 8-GB double arrays
  1-8 threads affinitized to a single socket to avoid NUMA
Macro-benchmarks (in paper)
  TPC-C, TPC-H

## Slide 7: Power Breakdown (Scans)
Chart: # threads
CPU | 68.079 | 69.2062 | 69.6167 | 70.9077 | 71.5783 | 72.4467 | 72.9067 | 73.6587
DRAM | 31.921 | 30.7938 | 30.3833 | 29.0923 | 28.4217 | 27.5533 | 27.0933 | 26.3413
DRAM contribution is high even at 100% CPU
Even with 256 GB RDIMMs, DRAM contributes 30%

## Slide 8: Impact of Frequency Scaling
Chart: Memory Frequency (MHz)
| 800 | 1067 | 1333 | 1600
Scans | 1.3784 | 1.1997 | 1.0252 | 1
Aggregation | 0.78123 | 0.83751 | 0.96256 | 1
Most energy-efficient is not always the fastest
8 threads

## Slide 9: Memory Bandwidth Utilization
Chart: # threads
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
800 MHz | 11947.2007 | 19229.3465 | 21536.5112 | 22233.4787 | 22556.346 | 22634.5373 | 22633.0367 | 22582.94
1067 MHz | 13422.8868 | 22954.448 | 27502.6467 | 29330.53 | 29906.6727 | 29964.987 | 29910.9236 | 29882.6309
1333 MHz | 13981.8246 | 24629.055 | 32009.721 | 34803.67 | 36171.9522 | 36425.925 | 36378.71 | 36288.7422
1600 MHz | 14336.0279 | 25496.8954 | 34952.3511 | 39610.9 | 41735.7762 | 42250.9871 | 42182.84 | 42113.8825
Bandwidth-intensive workloads suffer
(aggregation)

## Slide 10: Impact of Power-Down Modes
(aggregation)
Chart: # threads
| 1 | 8
Power | 0.87408 | 0.9909
Throughput | 0.99359 | 0.99668
No impact on performance or power
13% reduction in power

## Slide 11: Exploiting DRAM Idleness
Chart: # threads
| 1 | 8
Power-down (Scan) | 86 | 52
Active (Scan) | 14 | 48
Power-down (Agg) | 72 | 5
Active (Agg) | 27 | 95

MC good at predicting idleness
Memory Controller is conservative
>40% residency, yet negligible power savings

## Slide 12: Can We Do Better?
DRAM-aware memory layout
  Separate hot/cold data to enable longer idle time
DB-driven gear shifting
  Pairing data and power modes
Multitier memory and storage tiering.
  Rethinking anti-caching, 5-minute rule for two-level DRAM
Tiering-aware query optimization
  Making optimizer aware of access latencies

## Slide 13: Conclusion
Perfect storm
  MMDBs need more DRAM to meet application demands
  DRAM technology poses power-performance tradeoffs
Promise
  Frequency scaling/low-power modes can limit power draw
Hurdles
  Need software-driven DRAM DVFS and state transitions
  Need to redesigns MMDBs to exploit hardware features
  “It’s the memory, stupid!”
  - Richard L. Sites